High-performance door Albany RR500

Description:

Flexible high-performance door opening in vertical direction for interior and exterior use.

Special features:

- Push-pull technologie: Door curtain with lateral zipper teeth moved using the toothed top roll.

- Self-repairing knock-out capability: Automatically reset after a crash with the zip closure system.

- Flexible edge profile: Bottom profile made of flexible PVC material.

Side frames are made of galvanized steel with cover panels made of anodized aluminium. In the side frame is the guide rail for intake of the curtain (zipper closure).

Door curtain made of transparent PVC with reinforcement stripes, ultramarine (similar to RAL 5002)

or red (similar RAL 3002).

Top roll part of is made of stainless steel.

Wind protection: Zipper incl. automatic reset after crash.

Wind resistance: class 4 / class 3 if DW > 6000 mm EN 12424.

Bottom profile: made of flexible PVC material and automatic reset.

Knock-out capability with zip closure system. Should a collision occur, the curtain is automatically reset into the side frame if door is opened.

Drive unit: slip-on gear motor with catching device 0.75 kW.

Protection: IP 55.

Control system:

Frequency converter control system MCC, based on vector control including boost function at start-up. Graphic display and foil keypad for easy guided operation. Easy access to all important information for operation and service.

Control voltage: 24 V DC.

Supply voltage:

- 3/(N)PE/380/400/415/440/460/480V;50/60Hz;

- 3/(N) also with transformer available: 220V, 230V, 500V, 50/60 Hz;

- 1/N/PE: 220V, 230V 50/60 Hz speed reduced 25%.

Safety device:

- Door line photocell in the side frames,

- Electrical self-testing safety edge (inside rubber profile).

Manual activation by crank handle.

Opening / closing speed: MCC up to max. 1.0 /0.5 m/s

Size max.: 
(DW min./max) 1500 / 8000 mm

(DH min./max.) 2300 / 5500 mm

Make: Albany RR500

Options

Covers:

- Top roll cover made of anodized aluminum,

- Motor cover made of steel, powder coated (similar RAL 9006),

- Canopy, wall mounted.

Door curtain (alternatively):

- PVC with coloured reinforcements stripes, colour:

- Beige	(similar RAL 1014)

- Yellow	(similar RAL 1021)

- Orange	(similar RAL 2011)

- Green	(similar RAL 6018)

- White	(similar RAL 9016)

- Grey	(similar RAL 7035)

- NomaTex (fabric stiff across the grain), colour:

- Blue	(similar RAL 5005),

- Orange	(similar RAL 2009)

- Grey	(similar RAL 7038)

- Yellow	(similar RAL 1023)

- Red	(similar RAL 3000)

- NomaTex with vision panels

Miscellaneous:

- LED traffic light strip, mounted on external anodized aluminum bracket

- Heater at drive unit

- Drive unit UL-Version 3/(N) PE 220/230/460/480 V 60 Hz

- KNH Hand chain operator (without motor cover)

- Actuators

- Additional safety devices